## Slide 1
A-E20 · Darcy/storage approximation and derived diffusion
1e-06
1e-05
1e-04
1e-03
1e-06
1e-03
1e+00
1e+03
drainage length L_g (m)
tₚₒᵣₒ (s)
tₚₒᵣₒ = 1.5 s at 30 µm
event time 3 µs
slope 2: t ∝ L_g²
Darcy flow and diffusion
jₗ = −(k/μₗ) ∇pₚₒᵣₑ
∂p/∂t = Dₚₒᵣₒ ∇²p, Dₚₒᵣₒ = k M_d / μₗ
tₚₒᵣₒ ~ L_g² / Dₚₒᵣₒ = μₗ L_g² / (k M_d)
k = 10⁻¹⁷ m², M_d = 60 kPa, μₗ = 1 mPa s (prescribed
teaching values).
A 3 µs event is approximately undrained at 30 µm; local
solvent motion remains possible.
Permeability and modulus are inputs from characterisation; only the quadratic scaling with length is a result of the model.
Darcy/storage drainage time of Eq. A-E20.