## Slide 1
C1-E07 · Rayleigh–Plesset under the declared assumptions
0.0
0.5
1.0
1.5
1
2
3
t (µs)
R / R₀
with surface tension and viscosity
ideal: σ = μ = 0, same start
Every term is a pressure
ρ(RR̈ + 3Ṙ²/2)
+158 kPa
p_b − p∞
+187 kPa
−2σ/R
-21 kPa
−4μṘ/R
-7 kPa
t = 0.18 µs. Left side from finite-difference R̈ of the
solution; right side from the pressures. Mismatch 0.0 %.
One scalar equation for R(t): liquid inertia on the left, driving and resisting pressures on the right.
Gas pressure here is polytropic, p_b = p_g0 (R₀/R)^{3γ}, γ = 1.4, p_g0 = 1 MPa: an illustration of the closure still to be supplied.
Numerical integration of Eq. C1-E07; R₀ = 5 µm, ρ = 1000 kg/m³, p∞ = 101.3 kPa, σ = 0.072 N/m, μ = 1 mPa·s.