## Slide 1
C1-E25 · Declared impulse calculation and applicability diagnostics
Time scales of the declared impulse case (log axis, µs)
10⁻²
10⁻¹
10⁰
10¹
10²
10³
10⁴
10⁵
acoustic crossing
tₐ = L/c = 0.067 µs
pulse duration
τ = 0.5 µs
convective time
L/U = 33 µs
viscous time
L²/ν = 10 ms
Ratios of the declared case
Uτ/L = 0.015
τ ≪ convective time ✓
ντ/L² = 5×10⁻⁵
τ ≪ viscous time ✓
τ / tₐ = 7.5
τ is longer than the acoustic
crossing, so pressure equalises along
the column
Pressure impulse (Pa·s) and acoustic time (s) are different quantities: one measures the load delivered, the other how fast pressure
communicates.
Π₀ = Δpτ = 0.60 MPa × 0.50 µs = 0.30 Pa·s; U = 3.0 m/s; c = 1500 m/s; L = 100 µm; ν = 10⁻⁶ m²/s.