## Slide 1
C2-E08 · Thermal-contact boundary conditions
0.0
0.5
1.0
position across the contact
temperature (relative)
material A
material B
T_A − T_B = R_T qₙ
qₙ
qₙ (same)
Resistance at the contact
Flux continuity:
q_A·n = q_B·n = qₙ
Temperature jump:
T_A − T_B = R_T qₙ
R_T (m²K/W) is a property of the interface. The
same heat flows, but a temperature step builds up
and delays heating of side B.
Light is absorbed in A, yet B warms only after heat crosses the contact: absorbed energy is not delivered energy.
Contact conditions of Eq. C2-E08; profile is schematic.