## Slide 1
C2-E26 · Finite-inventory equilibrium benchmark
5
10
20
40
80
1e+04
1e+05
bubble radius R (µm)
pᵥ,PFC,eq (Pa)
40 °C: knee at 23 µm
50 °C: knee at 21 µm
liquid still present:
p = pₛₐₜ(T)
inventory exhausted:
p = mR_uT/(MV) falls as 1/R³
min[ saturation, inventory ]
pᵥ,eq = min[ pₛₐₜ(T_b), m_PFC,0 Rᵤ T_b /
(M_PFC V_b) ]
Until all liquid evaporates the pressure is
pinned at pₛₐₜ.
After that the finite inventory cannot supply
more vapor, so p falls as the bubble grows.
Assumes a closed, non-dissolving supply and
fast mass exchange.
Equilibrium benchmark for the 0.8535 ng inventory of a 5 µm core at two prescribed temperatures.
Finite-inventory benchmark of Eq. C2-E26 with pₛₐₜ from Eq. C2-E12.