## Slide 1
C2-E29 · Refined constant-pressure enthalpy path
Specific enthalpy gained along the constant-pressure path (kJ/kg)
290
300
310
320
25
50
75
100
125
temperature T (K)
H − H₀ (kJ/kg)
liquid: cₚ,l = 654 J/(kg K)
to Tₛₐₜ = 302.1 K
latent step
Lᵥ = 95 kJ/kg
vapor: cₚ,v (assumed 0.9 kJ/(kg K))
Each phase uses its own cₚ
Qᵢₛₒ = m [ ∫cₚ,l dT + Lᵥ(Tₛₐₜ, p) + ∫cₚ,v dT ]
Liquid heating stops at Tₛₐₜ = 302.1 K (1 bar),
not at T*.
Vapor heating from Tₛₐₜ to T* uses cₚ,v, a
different number.
The earlier estimate heated the liquid all the way
to T*.
Per kilogram: 5.9 kJ liquid + 95 kJ latent + 18.9 kJ vapor (cₚ,v is an assumed illustration).
Latent enthalpy still dominates, but the sensible parts must follow the phase actually being heated.
Refined constant-pressure path of Eq. C2-E29; Tₛₐₜ from Eq. C2-E12 at 1 bar.