## Slide 1
C3-E09 · Integrated solution on the inward branch
0.00
0.25
0.50
0.75
1.00
100
200
300
R / Rₘₐₓ
|Ṙ| (m/s)
χ = 0: |Ṙ| at Rₘₐₓ/2 = 21.6 m/s
χ = 1: |Ṙ| at Rₘₐₓ/2 = 17.6 m/s
χ = 3: |Ṙ| at Rₘₐₓ/2 = 13.7 m/s
Integrated solution
Ṙ = −√{ (2Δp_c/3ρ) (Rₘₐₓ³ − R³) / [R³ (1 + SR)] }
[R³(1 + SR) y] from Rₘₐₓ to R integrates to
(2Δp_c/3ρ)(Rₘₐₓ³ − R³).
The condition y(Rₘₐₓ) = 0 removes the constant.
The minus sign selects the inward branch.
Interaction (χ > 0) lowers the speed at every
radius.
Speed at half radius: 21.6 m/s for an isolated bubble, lower when neighbours add inertia.
Integrated speed of Eq. C3-E09 (Rₘₐₓ = 30 µm, ρ = 1000 kg/m³, Δp_c = 100 kPa).