## Slide 1
C3-E23 · Dynamic-pressure definition and steady momentum flux
Steady redirection of a jet
Uⱼ, Aⱼ
all axial momentum is removed; liquid leaves sideways
qⱼ = ½ρUⱼ², ṁ = ρA_jUⱼ
F_steady = ṁUⱼ = ρA_jUⱼ² = 2 qⱼ Aⱼ
Aⱼ = π(5 µm)² → F = 80 µN
Two very different pressure scales (MPa, log axis)
qⱼ = ½ρUⱼ²
0.509 MPa
ρ c Uⱼ (early rigid contact)
47.2 MPa
Dynamic pressure is a scale; it is not a pressure applied
over the whole surface.
Steady force follows from momentum flux with the same Uⱼ, ρ,
Aⱼ used elsewhere. The first nanoseconds of impact (second
bar) are about 90 times larger.
Eq. C3-E23 with the declared jet: Uⱼ = 31.915 m/s, dⱼ = 10 µm, ρ = 1000 kg/m³, c = 1480 m/s.