## Slide 1
C3-E30 · Worked finite jet mass, speed and pressure scales
The declared jet drawn to scale (10 µm diameter, 50 µm long)
Uⱼ
Lⱼ = 50 µm
dⱼ = 10 µm (cylinder height)
mass
mⱼ = ρ π dⱼ² Lⱼ / 4
3.927 ng
speed
Uⱼ = √(2Eⱼ/mⱼ), Eⱼ = 2 nJ
31.915 m/s
dynamic pressure
qⱼ = ½ρUⱼ²
0.5093 MPa
early rigid contact
ρ c Uⱼ (c = 1480 m/s)
47.23 MPa
momentum
Pⱼ = mⱼ Uⱼ; 25 jets: 25 Pⱼ
1.2533×10⁻¹⁰ N s;
3.1333×10⁻⁹ N s
The state carried into Chapter 4 includes mass, energy
and momentum, not a pressure peak alone.
Worked finite jet of Eq. C3-E30 (ρ = 1000 kg/m³, uniform direction, full activation, independent cells).