## Slide 1
C4-E03 · Derived plate parameters under constitutive assumptions
One film, two thickness integrals
h_f
mid-plane
density ρ_f is uniform
m_A = ∫ρ_f dz = ρ_f h_f
D_f = E_f/(1−ν²) ∫z² dz = E_f h_f³ / [12(1−ν_f²)]
0
1
0
0.5
weight
z / h_f
inertia: 1
0
0.25
0
0.5
z²
stiffness: z²
h_f = 10 µm, E_f = 2 GPa, ν_f = 0.35: m_A = 23.300 g/m², D_f =
1.899e-07 N m.
Outer fibres dominate bending: thickness enters as h³, inertia
only as h.
Plate parameters of Eq. C4-E03 (ρ_f = 2330 kg/m³ for the film mass).