## Slide 1
C4-E15 · Derived second pair of radial integrations
Second pair of integrations: build w(r)
start
d/dr (r w′) = r g = p₀ r³ / (4D_f) + C₂ r
integrate
r w′ = p₀ r⁴ / (16D_f) + C₂ r² / 2 + C₃
C₃ = 0 (regular)
w′ = p₀ r³ / (16D_f) + C₂ r / 2
integrate
w = p₀ r⁴ / (64D_f) + C₂ r² / 4 + C₄
0
0.5
1
-2
-1
0
1
r / b
terms of 64D_f w / p₀b⁴
sum (dashed)
r² term
constant C₄
r⁴ term
The regular solution has three pieces: quartic (from the load), quadratic and constant (both
fixed by the clamp).
Right: the three terms (solid) add up to the final profile (dashed), using the constants found in Eq. C4-E16.
Radial integration of Eq. C4-E15; pieces drawn for C₂ = −p₀b²/(8D_f) and C₄ = p₀b⁴/(64D_f) (preview of Eq. C4-E16).