## Slide 1
C4-E23 · Checked teaching substitution
Teaching calculation, step by step
plate stiffness
D_f = E_f h_f³ / [12(1 − ν²)]
E_f = 2.00 GPa, h_f = 10.0 µm, ν = 0.35
D_f = 1.899335e-07 N m
critical pressure
p₀,crit = √(128 D_f Γ) / b²
Γ = 0.10 J/m², b = 100 µm
p₀,crit = 155.921 kPa
inputs
E_f, h_f, ν, Γ, b
D_f
1.899e-07 N m
√(128 D_f Γ)
1.5592e-03
÷ b²
155.92 kPa
The 156 kPa threshold is conditional: it holds for this plate, this interface energy and this geometry, with pressure
maintained.
It is far below the 47 MPa early-contact scale of Chapter 3, but the pulse lasts only nanoseconds.
Checked substitution of Eq. C4-E23 (all inputs are declared teaching values).