## Slide 1
C4-E27 · Cohesive admissibility teaching calculation
Cohesive admissibility check with the teaching numbers
given
Γ = 0.005 J/m²
Tₘₐₓ = 0.10 MPa
Kₙ = 10¹³ Pa/m
δ₀ = Tₘₐₓ / Kₙ
10⁵ / 10¹³ = 1.0×10⁻⁸ m = 10 nm
δ_c = 2Γ / Tₘₐₓ
2(0.005) / 10⁵ = 1.0×10⁻⁷ m = 100 nm
δ₀ (peak)
10 nm
δ_c (final)
100 nm
δ_c is ten times δ₀: the law has a distinct softening stage, so it is admissible (δ₀ < δ_c).
These are stipulated teaching values, not measured properties of a real interface.
Admissibility calculation of Eq. C4-E27.