## Slide 1
C4-E41 · Transient plate power identity under fixed clamps
Power ledger (schematic)
0
0.5
1
1.00
applied work
-0.25
− cohesive loss
0.75
= stored + moving
d(K_f + U_b + U_T)/dt = ∫ p_load ẇ dA − ∫ t_coh ẇ dA
Each term has units of watts.
Multiply the balance by ẇ and integrate
inertia
∫ m_A ẅ ẇ dA = dK_f/dt
bending
∫ D_f ∇⁴w ẇ dA = dU_b/dt
tension
−∫ T₀ ∇²w ẇ dA = dU_T/dt
These identities need the fixed clamp: boundary power terms are zero.
Reading: the film cannot gain energy except through the work of
the load, minus what the cohesive layer takes.
Plate power identity of Eq. C4-E41; waterfall values are illustrative.