## Slide 1
C5-E12 · Axisymmetric compressible flow equations of the COMSOL model
Mass
∂ₜρ + ∇·(ρu) = 0
Momentum
ρ Du/Dt = −∇p + ∇·(viscous stress)
Liquid law
ρ(p) = ρ_j [(p + Π)/(p_j + Π)]^(1/γ)
Fields (axisymmetric)
ρ, p
u_r, w
viscosity μ = 1 mPa s
Same liquid as the C++ reference, plus radial motion and a small viscosity. No gas phase.
Schematic of Eq. (C5-E12).