## Slide 1
C5-E13 · Boundary and initial conditions of the axisymmetric model
plane z = 2a
band z ≤ 0.15 a
z = 4a
z = 0
r = 0
r = a
U
outlet at p_j
Setup
Compressible laminar flow, axisymmetric
Liquid law: Eq. (C5-E01), μ = 1 mPa s
Slip wall z = 0; inflow z = 4a
Free outlet r = a (confined case: slip)
Free triangles, global h_max = 0.025 a
Time output every 0.001 ns in the band runs
Band refinement sequence
band h = a/40
16,176 elements
band h = a/80
18,468 elements
band h = a/160
26,776 elements
band h = a/320
57,668 elements
Schematic; mesh lines are indicative, not the actual triangulation.