## Slide 1
C5-E01 · Adopted barotropic stiffened-gas law and exact sound speed
1.00
1.02
1.04
1.06
1.08
0
50
100
150
200
250
Density ratio ρ / ρ_j
Absolute pressure (MPa)
reference state (ρ_j, p_j)
behind the barotropic shock: ρ_1 / ρ_j = 1.0596
Liquid law
p(ρ) = (p_j + Π)(ρ / ρ_j)^γ − Π
γ = 4.4, Π = 600 MPa
Sound speed
c² = dp/dρ = γ (p + Π) / ρ
c_0 = 1626.447 m/s
Pressure depends on density alone;
not derived from first principles.
Curve computed from Eq. (C5-E01).

## Slide 2
C5-E02 · Rigid-wall limit of the Chapter 3 acoustic matching
Liquid, Z_l = ρ c
speed U
Wall, Z_r → ∞
Contact velocity v_i = Z_l U / (Z_l + Z_r)
v_i → 0 as Z_r → ∞
Contact pressure p = Z_l Z_r U / (Z_l + Z_r)
p → Z_0 U, Z_0 = ρ_j c_0
Numbers at U = 99.027 m/s
Z_0 = 1.6234 × 10⁶ Pa s/m
Z_0 U = 160.765 MPa
p_A = p_j + Z_0 U = 160.867 MPa
Linear estimate: valid for U/c_0 ≪ 1
Schematic of Eq. (C3-E24) in the limit Z_r → ∞. Not to scale.

## Slide 3
C5-E03 · Mass and momentum jump across the stopping shock
wall z = 0
shock front, lab speed S = U_s − U
incoming speed U
Behind the shock
at rest
ρ_1, p_1
Ahead of the shock
ρ_j, p_j
In the shock frame: liquid enters at U_s and leaves at U_s − U
Mass: ρ_1 (U_s − U) = ρ_j U_s
Momentum: p_1 − p_j = ρ_j U_s U
Velocity ratio x = U / U_s = 1 − ρ_j / ρ_1
Schematic of Eq. (C5-E03); distances are not to scale.

## Slide 4
C5-E04 · Energy-conserving Hugoniot pressure in closed form
0
50
100
150
0
100
200
300
Impact speed U (m/s)
Absolute wall pressure (MPa)
Curves
Hugoniot p_H (energy kept)
Barotropic p_B (density-only)
Acoustic p_A = p_j + Z_0 U
At U = 99.027 m/s
p_H = 174.623 MPa
p_B = 174.155 MPa
p_A = 160.867 MPa
p_B is 0.268% below p_H
Curves computed from Eqs. (C5-E02), (C5-E04) and (C5-E05).

## Slide 5
C5-E05 · Barotropic shock pressure used by both solvers
155
160
165
170
175
Absolute wall pressure at U = 99.027 m/s (MPa)
Acoustic p_A
160.867
Barotropic p_B
174.155
Hugoniot p_H
174.623
p_B is 0.268% below p_H: the energy equation is dropped.
p_A is 7.9% below p_H: the linear estimate ignores compression.
Values from Eqs. (C5-E02), (C5-E04) and (C5-E05).

## Slide 6
C5-E06 · Area-weighted wall observer and dimensionless time
a
core
Wall z = 0 seen from above
Observer
p̄_R = (2 / R²) ∫₀ᴿ p r dr
weight 2r dr / R² is the disk area element
R = a: full sensor
R = a/2: centre
Edge release
Front moves inward from r = a at c_0.
At τ = c_0 t / a the annulus a(1−τ) < r ≤ a has relaxed.
Area fraction f_rel = 1 − (1 − τ)².
At the peak: τ = 0.0472, f_rel = 0.0921
Full release would give 0.908 p_H
Schematic; annulus width is exaggerated for legibility.

## Slide 7
C5-E07 · Edge-release scale estimate for the finite sensor
0
0.2
0.4
0.6
0.8
1
0
0.25
0.5
0.75
1
τ = c_0 t / a
Fraction
Curves
f_rel = 1 − (1 − τ)²: released fraction
(1 − τ)²: full-release estimate
COMSOL p̄_a / p_H (band a/160)
Dotted line: peak at τ = 0.0472
f_rel = 0.0921; estimate 0.908
The estimate sets the sign
and size of the gap,
not its digits.
Estimate from Eq. (C5-E07); white curve from B00625_history.csv.

## Slide 8
C5-E08 · Incident mass and kinetic-energy flux through the observation plane
0
0.2
0.4
0.6
0.8
1
1.2
1.4
Time from first contact (ns)
incident window t_w = 1 ns
reflected shock returns to z = 2a at about 1.20 ns
Flux through the plane z = 2a
mass flow ṁ = ρ_j U π a² = 3.1053 × 10⁻⁷ kg/s
energy flux K̇ = ½ ρ_j U³ π a² = 1.5226 mW
K (1 ns) = K̇ · 1 ns = 1.5226 pJ
What the flux is not
Liquid energy crossing a plane.
A rigid wall does not move,
so it receives no work.
Numbers for a = 1 µm and U = 99.02724 m/s.

## Slide 9
C5-E09 · Dimensionless groups and validity range of the model
Mach number
M = U / c_0 = 0.0609
tested 0.031 to 0.092
Sound crossing of the radius
t_a = a / c_0 = 0.615 ns
for a = 1 µm
Compression behind the shock
ρ_1 / ρ_j = 1.0594
only 5.9% denser
Barotropic against energy law
(p_H − p_B) / p_H = 0.268%
at the nominal speed
Small Mach number and small compression let the density-only law stand in for the energy law.
Values from Eqs. (C5-E04) and (C5-E05) and the sensitivity cases.

## Slide 10
C5-E10 · One-dimensional conservative equations of the reference solver
0
1
2
3
0
1
2
3
4
Time from first contact (ns)
z (µm)
inflow boundary z = H
behind the shock:
at rest
ahead:
ρ_j, −U
Wave pattern
Barotropic shock: S = 1661.9 m/s
reaches H = 4 µm at 2.41 ns
Wall: u = 0 (mirror ghost state)
Inflow: (ρ_j, −U)
Conservative form lets the
shock move at the right speed.
Space-time sketch of Eq. (C5-E10); S from Eq. (C5-E05).

## Slide 11
C5-E11 · Rusanov flux with Heun time stepping
wall
cell 1
N
mirror ghost state
inflow ρ_j, −U
H = 4 µm, N = 4000, Δz = 1 nm
Face flux (Rusanov)
F = ½(F_L + F_R) − ½ α (Q_R − Q_L)
α = max(|u_L| + c_L, |u_R| + c_R)
Time step (Heun)
predictor Q* = Qⁿ + Δt L(Qⁿ)
Qⁿ⁺¹ = Qⁿ + ½ Δt [L(Qⁿ) + L(Q*)]
Wall pressure read from the cell next to the wall
Schematic of the discretization of Eqs. (C5-E10) and (C5-E11); only ten of 4000 cells are drawn.

## Slide 12
C5-E12 · Axisymmetric compressible flow equations of the COMSOL model
Mass
∂ₜρ + ∇·(ρu) = 0
Momentum
ρ Du/Dt = −∇p + ∇·(viscous stress)
Liquid law
ρ(p) = ρ_j [(p + Π)/(p_j + Π)]^(1/γ)
Fields (axisymmetric)
ρ, p
u_r, w
viscosity μ = 1 mPa s
Same liquid as the C++ reference, plus radial motion and a small viscosity. No gas phase.
Schematic of Eq. (C5-E12).

## Slide 13
C5-E13 · Boundary and initial conditions of the axisymmetric model
plane z = 2a
band z ≤ 0.15 a
z = 4a
z = 0
r = 0
r = a
U
outlet at p_j
Setup
Compressible laminar flow, axisymmetric
Liquid law: Eq. (C5-E01), μ = 1 mPa s
Slip wall z = 0; inflow z = 4a
Free outlet r = a (confined case: slip)
Free triangles, global h_max = 0.025 a
Time output every 0.001 ns in the band runs
Band refinement sequence
band h = a/40
16,176 elements
band h = a/80
18,468 elements
band h = a/160
26,776 elements
band h = a/320
57,668 elements
Schematic; mesh lines are indicative, not the actual triangulation.

## Slide 14
C5-E14 · Observers evaluated in the COMSOL model
U
plane z = 2a
z = 4a
z = 0
edge release
sensor r ≤ a (full)
centre r ≤ a/2
2a
Axisymmetric: wall z = 0, axis r = 0
Liquid column radius a, length 4a
Incoming speed U toward −z
Rigid slip wall at z = 0
Free side at r = a: pressure released to p_j
Plane z = 2a: incident mass and energy flux
Wall disk r ≤ a: area-weighted pressure
First contact at t = 0. Liquid only; no gas, no cavitation.
Model schematic; geometry is not to scale.

## Slide 15
C5-E15 · Relative error and successive-refinement change
155
160
165
170
175
180
Peak full-sensor pressure (MPa)
band h = a/40
16,176 elements
166.593
band h = a/80
18,468 elements
163.299
band h = a/160
26,776 elements
162.579
band h = a/320
57,668 elements
162.608
p_H = 174.623 MPa
Successive change
a/40 → a/80: 1.98%
a/80 → a/160: 0.44%
a/160 → a/320: 0.02%
Converged peak
162.6 MPa = 0.931 p_H
Denominator of each change:
the previous, coarser value
Values read from B025, B0125, B00625 and B003125 history files.

## Slide 16
C5-E16 · Time-integrated momentum and mass balance of the confined model
0.0001
0.001
0.01
0.1
1
10
Relative size (%), logarithmic axis
5% engineering line
Time step (strict vs automatic)
0.74%
Momentum balance (confined)
0.106%
Mass balance (confined)
0.018%
Plateau, C++ vs COMSOL
0.032%
Wave history L2, C++ vs COMSOL
0.034%
Centre disk vs p_H (converged)
0.143%
Incident speed, plane z = 2a
< 1e-5
Every bar compares a result with its own stated reference; none compares a model with an experiment.
Values from CH6_CH8_RESULTS.json, CPP_vs_COMSOL_wall_history.json and BAND_RESULTS.json.

## Slide 17
C5-E17 · Cross-solver comparison metrics for the confined column
0
0.5
1
1.5
2
0
50
100
150
200
Time from first contact (ns)
Absolute wall pressure (MPa)
p_H = 174.623 MPa
p_B = 174.155 MPa
Window 0.2 to 2.0 ns
C++ finite volume
COMSOL
361 common samples
δ₂ = 0.034%
δ∞ = 0.096%
Plateau 174.205 vs 174.148 MPa
Difference 0.032%
Both curves from sources/rigid_wall_ch5: SL_history.csv and cpp1d_SL.csv.

## Slide 18
C5-E18 · Scaling collapse and spread of the finite-area factor
0
0.1
0.2
0.3
0.4
0
0.25
0.5
0.75
1
τ = c_0 t / a
p̄_a / p_H
Peak factor Λ of each case
0.926
0.928
0.930
0.932
0.934
U 50 m/s: 0.9309
U 99.03 m/s: 0.9310
U 150 m/s: 0.9303
a 0.5 µm: 0.9303
a 2 µm: 0.9314
Spread 0.12% of the mean.
Ranges are scenario choices,
not confidence intervals.
Curves and peaks computed from the five band-run histories.

## Slide 19
C5-E19 · Delivered rigid-wall relations and link to the Chapter 3 ceiling
155
160
165
170
175
180
Peak absolute wall pressure at U = 99.027 m/s (MPa)
Linear ceiling p_A
160.87 MPa
acoustic
Full sensor, r ≤ a
162.58 MPa
0.931 p_H (band a/160)
Centre disk, r ≤ a/2
174.62 MPa
p_H within 0.43%
High-pressure interval lasts about a / c_0 = 0.61 ns for a = 1 µm.
Nonlinear factor over the linear ceiling: U_s / c_0 = 1.0856.
Values from Eq. (C5-E19) and the converged band runs.

## Slide 20
C5-E20 · Reference formulas: speed bound and pressure map together
Chapter 3
energy E_av, mass m_j
bound
Speed ceiling
U ≤ √(2 E_av / m_j)
bound
Prescribed speed U
taken as given here
input
Pressure map
p_wall = f(U)
computed
centre: p_H
full sensor: 0.931 p_H
The bound limits the speed. The map converts a speed to a pressure.
The two claims meet only at the prescribed speed.
A bound is not a prediction; a map is not a measurement.
Chain of Eq. (C5-E20); Chapter 3 bound from Eq. (C3-E32).

## Slide 21
C5-E21 · Reference formulas: edge-release explanation of the finite-area factor
0
0.25
0.5
0.75
1
0.90
0.92
0.94
0.96
0.98
1.00
κ: share of the excess lost in the released annulus
Λ
computed Λ = 0.931, κ = 0.75
full release: 0.908
Reading
Λ ≈ 1 − κ f_rel(τ_pk)
τ_pk = 0.0472, f_rel = 0.0921
κ = 0 : no loss, Λ = 1
κ = 1 : full release, Λ = 0.908
Simulation lies in between,
so about a quarter of the excess stays.
Line from Eq. (C5-E21); the computed Λ is from the converged band runs.

## Slide 22
C5-E22 · Reference formulas: validity range and limits of the verification
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
Impact Mach number M = U / c_0
tested: 0.031 to 0.092
nominal 0.0609
Speed axis
U = 50 m/s → M = 0.031
U = 150 m/s → M = 0.092
Inside the model
• Liquid only, barotropic stiffened-gas law
• Rigid flat slip wall, free jet side
• First arrival, τ = c_0 t / a ≤ 1
• Jet radius 0.5 to 2 µm
Outside the model
• Gas cushion, splash, cavitation
• Elastic wall; pressure after τ ≈ 1
• Bubble-to-jet physics upstream
• Any experiment: not established
Ranges taken from the five sensitivity cases and the model assumptions.